## Slide 2: Analysis of FPAs in the LHC RB circuit
Christoph Obermair, TE-MPE-CB Lukas Felsberger, TE-MPE-MI Franz Pernkopf, TU-Graz Andrea Apollonio, TE-MPE-CB Daniel Wollmann, TE-MPE-CB

## Slide 3: Introduction to Accelerators
Principle: Accelerate particles with electric field, and analyze collissions with target.
Types:
Linear accelerators - Linear accelerator 4 (Linac4)
  Limitation to high collission energy is electric field
  Breakdowns can destry radio frequency cavities
Circular accelerators - Large Hadron Collider (LHC)
  Limitation to high collission energy is electric field
  Quenches can destroy magnets
Current LHC status: LHC page 1
Lorentz Force
CLIC concept image

## Slide 4: Large Hadron Collider - LHC
11/7/2022
LHC Facts | 
Cost of the LHC | 4332 MCHF
Length | 26 659 m
Dipole operating temperature | -271.3°C
Cost per magnet | ~ 1 MCHF
Number of main dipoles | 1232
Power consumtion | 1.3 TWh/a
Number of circuits | 8
Stored energy per circuit | 1.1 GJ (380-ton TGV @ 50km/h)

## Slide 5: Quench Protection
Quench is biggest threat to LHC dipole magnets
Different types of quench:
  Primary quench
  Secondary quench: GHe propagation, EM disturbance,..
Quench Protection:
  Bypass Diode
  Quench Heater
Quenches with destructed magnets:
2008 (~100 destroyed magnets – splice opened)
2021 HWC (1 destroyed magnet - interturn short in coil)
  Possible precursor detected 1 month before
  Precursor: Oscillation in U_Diode Voltage
Goal: Further precursors?
Critical surface NbTi

## Slide 6: Quench Protection: U-Diode
PC Switch off
1st EE switch off
2nd EE switch off
Secondary quench
Interesting area

## Slide 7: Hardware
Diode
Energy Extraction Resistance

## Slide 8: Existing Database Overview
 | Signal | 2014-2020 | 2021 | # events
Real Data | U_DIODE_NXCALS | P | P | 867
 | U_DIODE_PM | P | P | 629
 | I_MEAS | P | P | 896
 | U_QSO, U_1, U_2 | P | P | 893
 | I_EARTH_PCNT | P | P | 895
 | I_EARTH | P | P | 629
 | I_HDS, U_HDS | P | P | 896
 | EEUDumpResPM | P | P | 896
Simulations | V(0v_magf*) | P | P | 875
 | I(r1_warm) | P | P | 875
 | V(10,11), V(18,19) | P | P | 875
#events |  | 267 | 629 | 560/896
Filtered events
Data overview

## Slide 9: El. Vs Phys. Position

## Slide 10: Position Frequency (FP) Map

## Slide 11: Non-Negative Matrix Factorization

## Slide 12: NMF vs. VQ vs. PCA
  number of images
  non negative pixel values
  number of components
  … reconstructed images
  … basis matrix (components)
  … coefficient matrix (Presence of components)
Constrains:
Non-Negative Matrix Factorization (NMF):
  must contain positive values
  Each face is additive combination of parts-based representation
Vector Quantization (VQ) / K-means:
  columns must be one hot encoded
  contains prototype faces
Principal Component Analysis (PCA):
  rows and columns must be orthogonal
  Each face is linear combination of “Eigenfaces”
NMF Objective Function:
, s.t.
https://www.nature.com/articles/44565
https://proceedings.neurips.cc/paper/2000/file/f9d1152547c0bde01830b7e8bd60024c-Paper.pdf

## Slide 13: How are the FP-maps composed?
Event:
RB_RB.A78_1617170255140000000
2021-03-31 07:57:35.120000
Common Oscillation
Physical Propagation
Electrical Propagation
Power Converter
Energy Extraction

## Slide 14: NMF on Position Frequency Maps
number of events * positions (560 x 154)
number of frequencies (0-360Hz)
number of components (1-10)
… reconstructed event at position
… components
… presence of components
NMF Objective Function:
... L1 Regularization
... L2 Regularization
... Orthogonal Regularization
s.t.
https://www.nature.com/articles/44565
https://proceedings.neurips.cc/paper/2000/file/f9d1152547c0bde01830b7e8bd60024c-Paper.pdf

## Slide 15: How are the FP-maps composed?
Event:
RB_RB.A78_1617170255140000000
2021-03-31 07:57:35.120000
Common Oscillation
Physical Propagation
Electrical Propagation
Power Converter
Energy Extraction

## Slide 16: NMF on Position Frequency Maps
Parameter: n_components=10,
init='nndsvd', tol=1e-3, l1_ratio=0.5, regularization='both', alpha=1

## Slide 17: NMF on Position Frequency Maps

## Slide 18: Next Steps
Find normal components -> optimize regularization + hyperparameters for NMF
Improve NMF:
  Normalize components in each run
  Trainable non-trainable components
Fix normal components (no update in )-> Find anomaly component:
  Which component occurs in faulty magnets
  How does component weight change over time

## Slide 19: NMF sensitivity analysis
Values to vary:
  Initialization:
    'nndsvd': Nonnegative Double Singular Value Decomposition (NNDSVD)
    'nndsvda': NNDSVD with zeros filled with the average of X
  Regularization:
    None, L1, L1+L2, L2
    On Transformation (H), and Components + Transformation (W + H)
    Weight
    Orthogonal Loss
  Shuffle: True, False
*SVD based initialization: A head start for nonnegative matrix factorization

## Slide 20: 'nndsvd vs 'nndsvda'
Assumption: L1 & L2 regularization
nndsvda Initialization
nndsvd Initialization

## Slide 21: 'nndsvd vs 'nndsvda'
Assumption: L1 & L2 regularization

## Slide 22: 'nndsvd vs 'nndsvda'
Assumption: L1 & L2 regularization (weight =1), 8 components
Conclusion: nndsvd slightly better, nndsvda is much faster
nndsvda
nndsvd

## Slide 23: 'nndsvd vs 'nndsvda'
Assumption: L1 & L2 regularization (weight =3), 8 components
Conclusion: nndsvd slightly better, nndsvda is faster (due to stopping criterion)
nndsvda
nndsvd

## Slide 24: Gifs Hyperparamters

## Slide 25: Regularization: L1 (l1_ratio=1) vs. L2 (l1_ratio=0)

## Slide 26: Regularization: L1 Weight

## Slide 27: Regularization: L2 Weight

## Slide 28: Regularization: L1+L2 Weight

## Slide 29: Regularization: Orthogonal Loss

## Slide 30: Regularization: Orthogonal Loss + L1+L2

## Slide 31: Plots Hyperparameters

## Slide 32: Regularization: None, L1, L1+L2, L2
Assumption: nndsvda, On Components + Transformation (W + H)

## Slide 33: Regularization: None, L1, L1+L2, L2
Conclusion: L1+L2 lead to best result
None
L1+L2

## Slide 34: Regularization: None, L1, L1+L2, L2
Conclusion: L1+L2 lead to best result
L1
L2

## Slide 35: Regularization: “both”, “transformation”
Assumption: nndsvda
Conclusion: H values get smaller and smaller, does not converge
None
L1+L2 on H

## Slide 36: Weight & Shuffling
Assumption: nndsvda, On Components + Transformation (W + H), L1 + L2, 6 components
Conclusion: shuffling reduces variance of results
Alpha: weight of regularization

## Slide 37: Weight & Shuffling
Assumption: nndsvda, On Components + Transformation (W + H), L1 + L2, 6 components
Conclusion: shuffling reduces variance of results
Alpha: weight of regularization
alpha = 0
alpha = 4

## Slide 38: Weight & Shuffling
Assumption: nndsvda, On Components + Transformation (W + H), L1 + L2, 10 components
Conclusion: shuffling reduces variance of results
Alpha: weight of regularization

## Slide 39: Weight & Shuffling
Assumption: nndsvda, On Components + Transformation (W + H), L1 + L2, 10 components
Conclusion: shuffling reduces variance of results
Alpha: weight of regularization
alpha = 0
alpha = 2.5

## Slide 40: Orthogonal Loss