## Slide 2: Analysis of FPAs in the LHC RB circuit
Christoph Obermair, TE-MPE-CB Lukas Felsberger, TE-MPE-MI Franz Pernkopf, TU-Graz Andrea Apollonio, TE-MPE-CB Daniel Wollmann, TE-MPE-CB

## Slide 3: Introduction to Accelerators
Principle: Accelerate particles with electric field, and analyze collissions with target.
Types:
Linear accelerators - Linear accelerator 4 (Linac4)
  Limitation to high collission energy is electric field
  Breakdowns can destry radio frequency cavities
Circular accelerators - Large Hadron Collider (LHC)
  Limitation to high collission energy is electric field
  Quenches can destroy magnets
Current LHC status: LHC page 1
Lorentz Force
CLIC concept image

## Slide 4: Large Hadron Collider - LHC
10/24/2022
LHC Facts | 
Cost of the LHC | 4332 MCHF
Length | 26 659 m
Dipole operating temperature | -271.3°C
Cost per magnet | ~ 1 MCHF
Number of main dipoles | 1232
Power consumtion | 1.3 TWh/a
Number of circuits | 8
Stored energy per circuit | 1.1 GJ (380-ton TGV @ 50km/h)

## Slide 5: Quench Protection
Quench is biggest threat to LHC dipole magnets
Different types of quench:
  Primary quench
  Secondary quench: GHe propagation, EM disturbance,..
Quench Protection:
  Bypass Diode
  Quench Heater
Quenches with destructed magnets:
2008 (~100 destroyed magnets – splice opened)
2021 HWC (1 destroyed magnet - interturn short in coil)
  Possible precursor detected 1 month before
  Precursor: Oscillation in U_Diode Voltage
Goal: Further precursors?
Critical surface NbTi

## Slide 6: Quench Protection: U-Diode
PC Switch off
1st EE switch off
2nd EE switch off
Secondary quench
Interesting area

## Slide 7: Hardware
Diode
Energy Extraction Resistance

## Slide 8: Existing Database Overview
 | Signal | 2014-2020 | 2021 | # events
Real Data | U_DIODE_NXCALS | P | P | 867
 | U_DIODE_PM | P | P | 629
 | I_MEAS | P | P | 896
 | U_QSO, U_1, U_2 | P | P | 893
 | I_EARTH_PCNT | P | P | 895
 | I_EARTH | P | P | 629
 | I_HDS, U_HDS | P | P | 896
 | EEUDumpResPM | P | P | 896
Simulations | V(0v_magf*) | P | P | 875
 | I(r1_warm) | P | P | 875
 | V(10,11), V(18,19) | P | P | 875
#events |  | 267 | 629 | 560/896
Filtered events
Data overview

## Slide 9: El. Vs Phys. Position

## Slide 10: Position Frequency Map

## Slide 11: Generalization
To calculate statistics, quench must occur at same position
Not consider events with secondary quenches
Split into
MAIN: Half where quench occurred
MIRROR: Other Half

## Slide 12: Quantiles
1st quantile
median
3rd quantile

## Slide 13: Find Peaks
302.1 Hz
65.4 Hz
143.3 Hz
183.8 Hz

## Slide 14: Find Peaks

## Slide 15: Voltage = f(Quantile)

## Slide 16: Non-Negative Matrix Factorization

## Slide 17: NMF vs. VQ vs. PCA
  number of images
  non negative pixel values
  number of components
  … reconstructed images
  … basis matrix (building blocks)
  … coefficient matrix (Presence of building blocks)
Constrains:
Non-Negative Matrix Factorization (NMF):
  must contain positive values
  Each face is additive combination of parts-based representation
Vector Quantization (VQ) / K-means:
  columns must be one hot encoded
  contains prototype faces
Principal Component Analysis (PCA):
  rows and columns must be orthogonal
  Each face is linear combination of “Eigenfaces”
NMF Objective Function:
, s.t.
https://www.nature.com/articles/44565
https://proceedings.neurips.cc/paper/2000/file/f9d1152547c0bde01830b7e8bd60024c-Paper.pdf

## Slide 18: Toy example
50x
30x
10x
1x
1x
1x

## Slide 19: Face example

## Slide 20: NMF for Position Frequency Maps
Oscillation from quench
Oscillation from border

## Slide 21: NMF for Position Frequency Maps
Challenges:
NMF with NAN values exists, but model adjustments make result much worse
Map parts have different origins
Oscillation from quench
Oscillation from border

## Slide 22: Preprocessing
Take half with more data
Interpolate nan values

## Slide 23: NMF - MIRROR
n_components = 4

## Slide 24: NMF - MIRROR
n_components = 6
Event with secondary quench ->
(anomaly in this dataset)

## Slide 25: NMF - MAIN
n_components = 4

## Slide 26: NMF - MAIN
n_components = 6

## Slide 27: Summary
Interpretation is key:
Check assumptions (e.g. scaling, processing)
Discussion with experts (no ML, algebra, statistics knowledge)
  Avoid over-engineering
Check NMF components:
  Do I just detect processing features (e.g. interpolation)

## Slide 29: Sanity Checks

## Slide 30: Kirchhoff
Challenges: (1) Sampling (2) Time-alignment

## Slide 31: FFT sanity check

## Slide 32: Data - Simulation

## Slide 33: Next Steps
Further improve plots, according to experts
Add FFT phase to track wave propagation
Find expected oscillation after quench adjust simulations (PSPICE)
Find oscillation anomalies precursor of magnet failure?
Possible method to find prototypes in position frequency map: NMF codebooks?

## Slide 34: Signal vs. scaled signal
Signal
Scaled Signal
Scaling:

## Slide 35: Overview of Data-Driven Models
High incorporation of knowledge and context
Fully data driven
Data-Driven Models
Manual Feature Engineering
Manual Threshold
Probabilistic
Classic Machine Learning
Automatic Feature Eningeering
Discriminative Deep Learning
Generative Deep Learning
GAN, RNN, ProtoNET
MLP, DCNN, FCN
SVM, Random Forrest, MLP
e.g. Busbar Resistance
e.g. QH Analysis
Physical Models
Dataset | 1. Feature analysis | 2. Find probabilities/correlations | 3. Finding concepts | 4. Predict parameters | 5. Generate data
1. U Diode Secondary Quench | Oscillation types | Oscillation evolvement |  |  | 
2. U Diode Primary Quench | Oscillation types | Oscillation evolvement | tSNE concepts | Predict sec. quench | 
3. U Diode Full Quench |  |  |  | Fit simulations | Reconstruct data

## Slide 36: 1. U Diode Secondary Quench

## Slide 37: Manual Feature Engineering
0
-2
-1
1
150
151
Classification of oscillations after secondary quenches

## Slide 38: Manual Feature Engineering
min_time, max_time
min_amplitude, max_amplitude
dU_min, dU_max
dstd_max
wiggle_area_pos, wiggle_area_elpos
dstd score:
  Using phys. position, el. position
  Different window functions
1
2
2
3
3
4
5
5

## Slide 39
1. Oscillation that only propagates electrically
Reason: electric coupling?
2. Oscillation that propagates physically and electrically
Reason: electric coupling through grounding?
Special case: Oscillation in only one magnet
3. Oscillation due to another quench in time window
Reason: coupling of magnets
4. Oscillation due to acquisition
Reason: acquisition
Manual Threshold

## Slide 40: Find Probabilities
Wiggle: How does the dstd score evolve in B28L8, compared to other magnets
Probabilistic

## Slide 41: 2. U Diode Primary Quench
U Diode PM
1st Energy Extraction
Frequency Domain

## Slide 42: Sunglass Threshold
Effect threshold to #quenches.
Filter: 20ms moving average

## Slide 43: Frequency Domain
Calculate real valued FFT out of scaled input for all magnets.
Scaling:

## Slide 44: 2D-tSNE Frequency Domain
tSNE input: all maximal frequencies per magnet (events, frequency)

## Slide 45: 2D-tSNE Frequency Domain
tSNE input: all maximal frequencies per magnet (events, frequency)

## Slide 46: 2D-tSNE Frequency Domain
tSNE input: all maximal frequencies per magnet (events, frequency)

## Slide 47: Finding concepts – tSNE overview
Example: Project 2D space to 1D space
2D space
1. Mapping distance between all points to distribution
KL-divergence
1D space
Random initialization
Mapping distance between all points to distribution ()
Distributions of 2D space should be similar to 1D space -> Minimize sum of all KL-divergences
Classic Machine Learning

## Slide 48: Finding concepts
Find different concepts of different anomalies in data
Example: Concepts in EE plateaus of U_diode PM
2D-tSNE axis 2
2D-tSNE axis 1
Classic Machine Learning

## Slide 49: 2. U Diode Full Quench

## Slide 50: Predict parameters
a.) Neural netlist optimization: Improve simulations with gradient descent
b.) Predict fast secondary quenches with CLIC approach: Use Explainable AI to see what the NN was looking at
Discriminative Deep Learning

## Slide 51: Generate data
Can ML generate data faster/more accurate than simulations? Using the same input
Optimization of decoder weights with MSE between real data and simulated data
Advantages:
  Decoder can create within seconds, more similar to real data
  Detection of anomalies with MSE
Disadvantage: Black box
Generative Deep Learning

## Slide 52: Generate data
Can ML generate data faster/more accurate than simulations?
Generative Deep Learning

## Slide 53: Discussion
Feature analysis:
Analyze both EE sunglasses, dependent on threshold, also within event
Find probabilities:
How does the dstd score evolve in B28L8, do other magnets evolve similarly?
Find concepts:
tSNE per magnet, look at frequency domain
Predict parameters:
Optimization of magnet parameter, research PSPICE optimization techniques
Generate data:
Simulation data will be improved
Check data integrity: sum of all u diode signals + ee signals should be 0
Also use: UQS0, Voltage feelers, Quench heaters
Genetische Optimierung,