## Slide 2: Interpretable Anomaly Detection in the LHC Main Dipole Circuit with Non-negative Matrix Factorization
Christoph Obermair, TE-MPE-CB
Acknowledgement:
Marvin Janitschke, TE-MPE-PE
Emmanuele Ravaioli, TE-MPE-PE
Mariusz Wozniak, TE-MPE-PE
Zinour Charifoulline, TE-MPE-PE
Lukas Felsberger, TE-MPE-MI
Daniel Wollmann, TE-MPE-CB
Aleksandra Mnich, TE-MPE-CB
Franz Pernkopf, TU-Graz

## Slide 3: LHC Main Dipole Circuit
Quench:
Part of coil exceeds critical surface Energy drops at this part
Quench protection:
  Quench detection with voltage on magnet
  Beam extraction: 350 MJ
  Magnet protection:
    Diode redirects current
    Quench heater heats up
  Energy extraction: 1.1 GJ
Diode
Energy Extraction
Beam Extraction

## Slide 4: Outline
Goal: Define and understand normal behavior, detect abnormal behavior of the main dipole (RB) circuit
Approach:
Extract frequencies in data Fast Fourier transform (FFT)
Group expected frequencies that occur together into components Non-Negative Matrix Factorization (NMF)
  Components help to understand normal behavior Causal Discovery
  Deviations help to detect abnormal behavior Outlier detection

## Slide 5: Select data
Signal:
U_diode from nQPS in PM
Region:
Plateaus after energy extraction Similar to transient measurement
Period:
2018, Quench + Snapshot data
Data size:
731 events x 154 magnets x 400 samples (0.375s)
*simulations done by Marvin Janitschke with STEAM framework
PC Switch off
1st EE switch off
2nd EE switch off
1st EE
Plateau
2nd EE
Plateau

## Slide 6: Fast Fourier transform
Extract frequencies in data

## Slide 7: Fast Fourier transform
Preprocessing necessary to minimize spectral leakage:
Subtract offset
Multiplication with window
Example signal: B21R3 on 2021-04-18 08:44:17

## Slide 8: Frequency Position Maps (FPM)
PC Switch off
1st EE switch off
2nd EE switch off
1st EE
Plateau
2nd EE
Plateau
fft
Normal event

## Slide 9: Non-Negative Matrix Factorization (NMF)
https://www.nature.com/articles/44565
https://proceedings.neurips.cc/paper/2000/file/f9d1152547c0bde01830b7e8bd60024c-Paper.pdf
Group expected frequencies that occur together into components
  Components help to understand normal behavior Causal Discovery
  Deviations help to detect abnormal behavior Outlier detection

## Slide 10: Method
0.0003
0.0036
Loss:
How to define ?
Manually define
Initialize randomly
Adjust iterativly until loss over all signals (763 * 154 * 2= 235 004) is minimal
Input
Components
Reconstruction
Weights
Example signal: B21R3 on 2021-04-18 08:44:17

## Slide 11: NMF Components
Component Index | Component | 3 Event Examples | Dominant Frequencies | Order of magnitude
0* |  |  | 3 Hz | 100mV
1 |  |  | 6 Hz | 100mV
2 |  |  | 20 Hz | 10mV

## Slide 12
Component Index | Component | 3 Event Examples | Dominant Frequencies [Hz] | Order of magnitude
3 |  |  | 67 Hz 184 Hz 302 Hz | 100mV
4 |  |  | 148 Hz | 1mV
5 |  |  | 107 Hz 220 Hz 260 Hz 370 Hz 478 Hz | 0.1mV
6 |  |  | Any | 100mV

## Slide 13: Causal Discovery
Understand normal behavior

## Slide 14: Causal Discovery
3Hz
Left over of voltage wave traveling along the chain of magnets by magnet inductance
Source Direction: Quench
Propagation: Physical
Oscillations caused by quench
Source Direction: Quench
Propagation: Electrical
Repetitive pattern within QPS crate, aliasing?
Source Direction: Quench
Propagation: QPS crate position
Oscillations from the direction of Power converter in RB.A78, aliasing?
Source Direction: Power converter in RB.A78
Propagation: Physical
Oscillations caused by quench
Source Direction: Quench
Propagation: Physical
6Hz
20Hz
65Hz
143Hz
478Hz
Offset
Frequency components along all magnets in event
Electromagnetic perturbation
Source Direction: Quench
Propagation: Physical
Electromagnetic perturbation + FFT smiring
Source Direction: Quench
Propagation: Physical
Normal event

## Slide 15: Outlier Detection
Detect abnormal behavior

## Slide 16: Outlier Detection
Components state frequencies, expected to occur
Normal event: Reconstruction with components possible (low loss)
Outlier event: Unexpected frequencies occur (high loss)
How to find an outlier:
Calculate NMF loss for each event (763)
Fit distribution to loss
Calculate p value for each event (763)
  probability of obtaining results at least as extreme as the observed
Outliers
Normal event
Normal

## Slide 17: Outliers
Goal: Find outliers robust to assumptions
Result shows boxplot of 280 different combinations of assumptions
All outliers occur during 1st EE Plateau closer in time to quench
3rd Quantil (Q3)
Q3 + 1.5 * Box length
Median
1st Quantil (Q1)
Box
length
Q1 - 1.5 * Box length

## Slide 18: Conclusion
Causal Discovery:
Detection of “normal” frequency components with Non-Negative Matrix Factorization Depending on the quench position, a typical FPM would look like this:
Outlier Detection:
Outliers are events which cannot be composed out of “normal” frequency components
Ongoing additional measurements, additional safety measures, possible replacement

## Slide 20: Backup Slides

## Slide 21: Aliasing
1.5kHz 1st Order lowpass direkt am Eingang und dann noch einen zweiten mit 1kHz vor dem ADC
High frequency components could potentially cause aliasing in results.
Anti-aliasing filters in the nQPS crates:
Two 1st order lowpass filters with 1.5 kHz and 1 kHz cutoff frequency*
Sampling frequency of nQPS crates: 1068 Hz
*provided by Jens Steckert

## Slide 22: Fast Fourier transform

## Slide 23: Fast Fourier transform
The FFT is an algorithm to calculate the discrete Fourier transform (DFT). The DFT is defined as:
Apply Hilbert transform: Multiply all but first sample of FFT amplitude with 2
Smearing

## Slide 24: Window data
Use Window:
Add Window gain: Divide with
Avoid smearing
Smearing
Wrong Amplitude
Smearing from DC

## Slide 25: Detrend data
Subtract trend:
Smearing of DC component interferes with low frequency component
Smearing from DC

## Slide 26: Backwards Path
Signal: B21R3 on 2021-04-18 08:44:17

## Slide 27: Non-Negative Matrix Factorization (NMF)
https://www.nature.com/articles/44565
https://proceedings.neurips.cc/paper/2000/file/f9d1152547c0bde01830b7e8bd60024c-Paper.pdf

## Slide 28: Objective Function
number of events * positions (560 x 154)
number of frequencies (0-360Hz)
number of components (1-5)
… reconstructed event at position
… components
… presence of components
NMF Objective Function:
, s.t.

## Slide 29: Backwards Path
Signal: B21R3 on 2021-04-18 08:44:17

## Slide 30: Causal Discovery

## Slide 31: Component 0 & 1: EM Perturbation
Filter: 20ms moving average
dV is measured similar to sunglass threshold
dV
dV

## Slide 32: Component 4 & 5

## Slide 33: Outlier Detection

## Slide 34: Assumptions
Preprocessing:
  Degree of detrend:
    0 - Offset
    1 - Linear Trend
  Window multiplication:
    none (best reconstruction, high smearing)
    hanning (lowest smearing, no reconstruction)
    hamming (low smearing , good reconstruction)
    barlett
    blackman
    flattop (high smearing, accurate amplitude)
    tukey
NMF:
  n_components (2-12)
  Distance measure*:
    Frobenius (Eu)
    Kullback-Leibler (KL)
280 x
* https://ieeexplore.ieee.org/stamp/stamp.jsp?arnumber=6410389
Assumptions for this plot:
Linear detrend
Hamming window
4 components
Frobenius distance

## Slide 35: RB.A78 - B28L8 – Intercoil short
Event with B28L8 quench before:
2021-03-28: „normal“ at EE plateaus

## Slide 36: RB.A12 - B11L2
A11L2, E4
B9L2, E153
B10L2, E152
A9L2, E3
No B11L2 quench before

## Slide 37: RB.A34 – B28R3
No B28R3 quench before
Most likely scenario of noise from simulations:
Partially emerging resistor, in parallel to diode
Degraded diode contact?